## Slide 1
Decimal Numbers |  |  |  |  | 
 | Base 10 |  |  |  | 
 | Each digit can hold 10 distinct values |  |  |  | 
 | 0-9 |  |  |  | 
 | Each additional digit position is 10x |  |  |  | 
 | 1000's | 100's | 10's | 1's | 
 | 5 | 4 | 6 | 2 | 
 | The value of 5462 is: |  |  |  | 
 | 5x1000 | 5000 |  |  | 
 | 4x100 | 400 |  |  | 
 | 6x10 | 60 |  |  | 
 | 2x1 | 2 |  |  | 
 |  | 5462 |  |  | 

## Slide 2
Binary Numbers |  |  |  |  |  |  | 
 |  | Base 2 |  |  |  |  | 
 |  | Each digit can hold 2 distinct values |  |  |  |  | 
 |  | 0-1 |  |  |  |  | 
 |  | Each additional digit position is 2x |  |  |  |  | 
128's | 64's | 32's | 16's | 8's | 4's | 2's | 1's
1 | 0 | 1 | 0 | 1 | 1 | 0 | 1
The value of 10101101 is: |  |  |  |  |  |  | 
1x128 | 128 |  |  |  |  |  | 
0x64 | 0 |  |  |  |  |  | 
1x32 | 32 |  |  |  |  |  | 
0x16 | 0 |  |  |  |  |  | 
1x8 | 8 |  |  |  |  |  | 
1x4 | 4 |  |  |  |  |  | 
0x2 | 0 |  |  |  |  |  | 
1x1 | 1 |  |  |  |  |  | 
 | 173 |  |  |  |  |  | 

## Slide 3
 | Octal Numbers |  |  |  | 
 | Base 8 |  |  |  | 
 | Each digit can hold 8 distinct values |  |  |  | 
 | 0-7 |  |  |  | 
 | Each additional digit position is 8x |  |  |  | 
 | 512's | 64's | 8's | 1's | 
 | 3 | 4 | 6 | 1 | 
 | The value of 3461 is: |  |  |  | 
 | 3x512 | 1536 |  |  | 
 | 4x64 | 256 |  |  | 
 | 6x8 | 48 |  |  | 
 | 1x1 | 1 |  |  | 
 |  | 1841 |  |  | 

## Slide 4
Hexadecimal Numbers |  |  |  |  |  | 
Base 16 |  |  |  |  | Hex Digits | 
Each digit can hold 16 distinct values |  |  |  |  | 0 | 
0-9 A-F |  |  |  |  | 1 | 
Each additional digit position is 16x |  |  |  |  | 2 | 
 |  |  |  |  | 3 | 
4096's | 256's | 16's | 1's |  | 4 | 
1 | 2 | C | E |  | 5 | 
 |  |  |  |  | 6 | 
The value of 12CE is: |  |  |  |  | 7 | 
1x4096 |  | 4096 |  |  | 8 | 
2x256 |  | 512 |  |  | 9 | 
12x16 |  | 192 |  |  | A | (10)
14x1 |  | 14 |  |  | B | (11)
 |  | 4814 |  |  | C | (12)
 |  |  |  |  | D | (13)
 |  |  |  |  | E | (14)
 |  |  |  |  | F | (15)

## Slide 5
Converting Binary to Decimal |  |  |  |  |  |  |  |  | 
Write out the binary digit values across the top |  |  |  |  |  |  |  |  | 
Starting with the least significant digit being 1 and multiplying by 2 for each digit. |  |  |  |  |  |  |  |  | 
Add up the digit values that have a digit of 1 |  |  |  |  |  |  |  |  | 
256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 | 
1 | 0 | 1 | 1 | 1 | 0 | 0 | 1 | 1 | 
256 |  |  |  |  |  |  |  |  | 
64 |  |  |  |  |  |  |  |  | 
32 |  |  |  |  |  |  |  |  | 
16 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
1 |  |  |  |  |  |  |  |  | 
371 | 101110011 in Binary = 371 in Decimal |  |  |  |  |  |  |  | 
 |  | Example A |  |  |  |  |  |  | 

## Slide 6
Converting Binary to Decimal |  |  |  |  |  |  |  |  | 
Write out the binary digit values across the top |  |  |  |  |  |  |  |  | 
Starting with the least significant digit being 1 and multiplying by 2 for each digit. |  |  |  |  |  |  |  |  | 
Add up the digit values that have a digit of 1 |  |  |  |  |  |  |  |  | 
128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 |  | 
1 | 0 | 1 | 1 | 0 | 1 | 1 | 0 |  | 
128 |  |  |  |  |  |  |  |  | 
32 |  |  |  |  |  |  |  |  | 
16 |  |  |  |  |  |  |  |  | 
4 |  |  |  |  |  |  |  |  | 
2 |  |  |  |  |  |  |  |  | 
182 |  |  |  |  |  |  |  |  | 
 | 10110110 in Binary = 182 in Decimal |  |  |  |  |  |  |  | 
 |  | Example B |  |  |  |  |  |  | 

## Slide 7
Converting Decimal to Binary |  |  |  |  |  |  |  |  |  |  |  |  | 
Write out the binary digit values across the top |  |  |  |  |  |  |  |  |  |  |  |  | 473
Starting with the least significant digit being 1 and multiplying by 2 for each digit. |  |  |  |  |  |  |  |  |  |  |  |  | -256
Write out the binary digit values until you write a number larger than the decimal value to be converted |  |  |  |  |  |  |  |  |  |  |  |  | 217
Starting with the most significant digit, subtract the digit value from the remaining decimal value |  |  |  |  |  |  |  |  |  |  |  |  | -128
If the subtraction results in a negative enter a 0 for that digit position, if it is positive enter a 1 |  |  |  |  |  |  |  |  |  |  |  |  | 89
 |  |  |  |  |  |  |  |  |  |  |  |  | -64
To convert the decimal number 473... |  |  |  |  |  |  |  |  |  |  |  |  | 25
 |  |  |  |  |  |  |  |  |  |  |  |  | -16
512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 |  |  |  | 9
0 | 1 | 1 | 1 | 0 | 1 | 1 | 0 | 0 | 1 |  |  |  | -8
 |  |  |  |  |  |  |  |  |  |  |  |  | 1
473 in Decimal = 111011001 in Binary |  |  |  |  |  |  |  |  |  |  |  |  | -1
(You can discard leading zero's) |  |  |  |  |  |  |  |  |  |  |  |  | 0
 | Example A |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 8
Converting Decimal to Binary |  |  |  |  |  |  |  |  |  |  |  |  | 
Write out the binary digit values across the top |  |  |  |  |  |  |  |  |  |  |  |  | 377
Starting with the least significant digit being 1 and multiplying by 2 for each digit. |  |  |  |  |  |  |  |  |  |  |  |  | -256
Write out the binary digit values until you write a number larger than the decimal value to be converted |  |  |  |  |  |  |  |  |  |  |  |  | 121
Starting with the most significant digit, subtract the digit value from the remaining decimal value |  |  |  |  |  |  |  |  |  |  |  |  | -64
If the subtraction results in a negative enter a 0 for that digit position, if it is positive enter a 1 |  |  |  |  |  |  |  |  |  |  |  |  | 57
 |  |  |  |  |  |  |  |  |  |  |  |  | -32
To convert the decimal number 377... |  |  |  |  |  |  |  |  |  |  |  |  | 25
 |  |  |  |  |  |  |  |  |  |  |  |  | -16
512 | 256 | 128 | 64 | 32 | 16 | 8 | 4 | 2 | 1 |  |  |  | 9
0 | 1 | 0 | 1 | 1 | 1 | 1 | 0 | 0 | 1 |  |  |  | -8
 |  |  |  |  |  |  |  |  |  |  |  |  | 1
377 in Decimal = 101111001 in Binary |  |  |  |  |  |  |  |  |  |  |  |  | -1
(You can discard leading zero's) |  |  |  |  |  |  |  |  |  |  |  |  | 0
 | Example B |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 9
Converting Octal to Binary |  |  |  |  |  |  |  |  |  |  |  | 
It takes 3 binary digits to represent all of the possible Octal digits. |  |  |  |  |  |  |  |  |  |  |  | 
Starting with the least significant digit write out each octal digit using 3 binary digits |  |  |  |  |  |  |  |  |  |  |  | 
Be sure to use all 3 binary digits including leading zero's |  |  |  |  |  |  |  |  |  |  |  | 
To convert the octal number 6472... |  |  |  |  |  |  |  |  | 4 | 2 | 1 | 
 |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 
 | 6 | 4 | 7 | 2 |  |  |  | 1 | 0 | 0 | 1 | 
 | 110 | 100 | 111 | 010 |  |  |  | 2 | 0 | 1 | 0 | 
 |  |  |  |  |  |  |  | 3 | 0 | 1 | 1 | 
 | 6472 in Octal = 110100111010 in Binary |  |  |  |  |  |  | 4 | 1 | 0 | 0 | 
 |  |  |  |  |  |  |  | 5 | 1 | 0 | 1 | 
 | Example A |  |  |  |  |  |  | 6 | 1 | 1 | 0 | 
 |  |  |  |  |  |  |  | 7 | 1 | 1 | 1 | 

## Slide 10
Converting Octal to Binary |  |  |  |  |  |  |  |  |  |  |  | 
It takes 3 binary digits to represent all of the possible Octal digits. |  |  |  |  |  |  |  |  |  |  |  | 
Starting with the least significant digit write out each octal digit using 3 binary digits |  |  |  |  |  |  |  |  |  |  |  | 
Be sure to use all 3 binary digits including leading zero's |  |  |  |  |  |  |  |  |  |  |  | 
To convert the octal number 1530... |  |  |  |  |  |  |  |  | 4 | 2 | 1 | 
 |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 
 | 1 | 5 | 3 | 0 |  |  |  | 1 | 0 | 0 | 1 | 
 | 001 | 101 | 011 | 000 |  |  |  | 2 | 0 | 1 | 0 | 
 |  |  |  |  |  |  |  | 3 | 0 | 1 | 1 | 
 | 1530 in Octal = 001101011000 in Binary |  |  |  |  |  |  | 4 | 1 | 0 | 0 | 
 | (You can now drop the leading zero's) |  |  |  |  |  |  | 5 | 1 | 0 | 1 | 
 |  |  |  |  |  |  |  | 6 | 1 | 1 | 0 | 
 | Example B |  |  |  |  |  |  | 7 | 1 | 1 | 1 | 

## Slide 11
Converting Binary to Octal |  |  |  |  |  |  |  |  |  |  |  | 
It takes 3 binary digits to represent all of the possible Octal digits. |  |  |  |  |  |  |  |  |  |  |  | 
Starting with the least significant digits chunk the binary number into 3 binary digit pieces. |  |  |  |  |  |  |  |  |  |  |  | 
Convert each chunk of 3 binary digits to an octal digit. |  |  |  |  |  |  |  |  |  |  |  | 
To convert the binary number 110100101... |  |  |  |  |  |  |  |  | 4 | 2 | 1 | 
 |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 
 |  |  | 110 | 100 | 101 |  |  | 1 | 0 | 0 | 1 | 
 |  |  | 6 | 4 | 5 |  |  | 2 | 0 | 1 | 0 | 
 |  |  |  |  |  |  |  | 3 | 0 | 1 | 1 | 
110100101 in Binary = 645 in Octal |  |  |  |  |  |  |  | 4 | 1 | 0 | 0 | 
 |  |  |  |  |  |  |  | 5 | 1 | 0 | 1 | 
 |  |  |  |  |  |  |  | 6 | 1 | 1 | 0 | 
 | Example A |  |  |  |  |  |  | 7 | 1 | 1 | 1 | 

## Slide 12
Converting Binary to Octal |  |  |  |  |  |  |  |  |  |  |  | 
It takes 3 binary digits to represent all of the possible Octal digits. |  |  |  |  |  |  |  |  |  |  |  | 
Starting with the least significant digits chunk the binary number into 3 binary digit pieces. |  |  |  |  |  |  |  |  |  |  |  | 
Convert each chunk of 3 binary digits to an octal digit. |  |  |  |  |  |  |  |  |  |  |  | 
To convert the binary number 10110101111... |  |  |  |  |  |  |  |  | 4 | 2 | 1 | 
 |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 
 |  | 010 | 110 | 101 | 111 |  |  | 1 | 0 | 0 | 1 | 
 |  | 2 | 6 | 5 | 7 |  |  | 2 | 0 | 1 | 0 | 
 |  |  |  |  |  |  |  | 3 | 0 | 1 | 1 | 
10110101111 in Binary = 2657 in Octal |  |  |  |  |  |  |  | 4 | 1 | 0 | 0 | 
 | I added a leading zero to the last chunk to make it 3 digits |  |  |  |  |  |  | 5 | 1 | 0 | 1 | 
 |  |  |  |  |  |  |  | 6 | 1 | 1 | 0 | 
 | Example B |  |  |  |  |  |  | 7 | 1 | 1 | 1 | 

## Slide 13: Octal to Decimal -- Decimal to Octal
The easiest way to convert Octal to Decimal and Decimal to Octal is to convert to Binary as an intermediate step.
(Unless of course you use a calculator)

## Slide 14
Converting Binary to Hexadecimal |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
It takes 4 binary digits to represent all of the possible hexadecimal digits. |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 4 | 2 | 1 | 
Starting with the least significant digits chunk the binary number into 4 binary digit pieces. |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 
Convert each chunk of 4 binary digits to a hexadecimal digit |  |  |  |  |  |  |  |  |  |  |  | 1 | 0 | 0 | 0 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  | 2 | 0 | 0 | 1 | 0 | 
To convert the binary number 100111010011... |  |  |  |  |  |  |  |  |  |  |  | 3 | 0 | 0 | 1 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  | 4 | 0 | 1 | 0 | 0 | 
 |  |  | 1001 | 1101 | 0011 |  |  |  |  |  |  | 5 | 0 | 1 | 0 | 1 | 
 |  |  | 9 | D | 3 |  |  |  |  |  |  | 6 | 0 | 1 | 1 | 0 | 
 |  |  |  |  |  |  |  |  |  |  |  | 7 | 0 | 1 | 1 | 1 | 
100111010011 in Binary = 9D3 in Hexadecimal |  |  |  |  |  |  |  |  |  |  |  | 8 | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  |  |  | 9 | 1 | 0 | 0 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  | A (10) | 1 | 0 | 1 | 0 | 
 | Example A |  |  |  |  |  |  |  |  |  |  | B (11) | 1 | 0 | 1 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  | C (12) | 1 | 1 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  |  |  | D (13) | 1 | 1 | 0 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  | E (14) | 1 | 1 | 1 | 0 | 
 |  |  |  |  |  |  |  |  |  |  |  | F (15) | 1 | 1 | 1 | 1 | 

## Slide 15
Converting Binary to Hexadecimal |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
It takes 4 binary digits to represent all of the possible hexadecimal digits. |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 4 | 2 | 1 | 
Starting with the least significant digits chunk the binary number into 4 binary digit pieces. |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 
Convert each chunk of 4 binary digits to a hexadecimal digit |  |  |  |  |  |  |  |  |  |  |  | 1 | 0 | 0 | 0 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  | 2 | 0 | 0 | 1 | 0 | 
To convert the binary number 100111010011101... |  |  |  |  |  |  |  |  |  |  |  | 3 | 0 | 0 | 1 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  | 4 | 0 | 1 | 0 | 0 | 
 |  | 0100 | 1110 | 1001 | 1101 |  |  |  |  |  |  | 5 | 0 | 1 | 0 | 1 | 
 |  | 4 | E | 9 | D |  |  |  |  |  |  | 6 | 0 | 1 | 1 | 0 | 
 |  |  |  |  |  |  |  |  |  |  |  | 7 | 0 | 1 | 1 | 1 | 
100111010011101 in Binary = 4E9D in Hexadecimal |  |  |  |  |  |  |  |  |  |  |  | 8 | 1 | 0 | 0 | 0 | 
 | I added a leading zero to the last chunk to make it 4 digits |  |  |  |  |  |  |  |  |  |  | 9 | 1 | 0 | 0 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  | A (10) | 1 | 0 | 1 | 0 | 
 | Example B |  |  |  |  |  |  |  |  |  |  | B (11) | 1 | 0 | 1 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  | C (12) | 1 | 1 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  |  |  | D (13) | 1 | 1 | 0 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  | E (14) | 1 | 1 | 1 | 0 | 
 |  |  |  |  |  |  |  |  |  |  |  | F (15) | 1 | 1 | 1 | 1 | 

## Slide 16
Converting Hexadecimal to Binary |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
It takes 4 binary digits to represent all of the possible hexadecimal digits. |  |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 4 | 2 | 1 | 
Starting with the least significant digit write out each hexadecimal digit using 4 binary digits |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 
Be sure to use all 4 binary digits including leading zero's |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 0 | 0 | 0 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  |  | 2 | 0 | 0 | 1 | 0 | 
To convert the hexadecimal number D58A... |  |  |  |  |  |  |  |  |  |  |  |  | 3 | 0 | 0 | 1 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  |  | 4 | 0 | 1 | 0 | 0 | 
 |  |  | D | 5 | 8 | A |  |  |  |  |  |  | 5 | 0 | 1 | 0 | 1 | 
 |  |  | 1101 | 0101 | 1000 | 1010 |  |  |  |  |  |  | 6 | 0 | 1 | 1 | 0 | 
 |  |  |  |  |  |  |  |  |  |  |  |  | 7 | 0 | 1 | 1 | 1 | 
D58A in Hexadecimal = 1101010110001010 in Binary |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  |  |  |  | 9 | 1 | 0 | 0 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  |  | A (10) | 1 | 0 | 1 | 0 | 
 | Example A |  |  |  |  |  |  |  |  |  |  |  | B (11) | 1 | 0 | 1 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  |  | C (12) | 1 | 1 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  |  |  |  | D (13) | 1 | 1 | 0 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  |  | E (14) | 1 | 1 | 1 | 0 | 
 |  |  |  |  |  |  |  |  |  |  |  |  | F (15) | 1 | 1 | 1 | 1 | 

## Slide 17
Converting Hexadecimal to Binary |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
It takes 4 binary digits to represent all of the possible hexadecimal digits. |  |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 4 | 2 | 1 | 
Starting with the least significant digit write out each hexadecimal digit using 4 binary digits |  |  |  |  |  |  |  |  |  |  |  |  | 0 | 0 | 0 | 0 | 0 | 
Be sure to use all 4 binary digits including leading zero's |  |  |  |  |  |  |  |  |  |  |  |  | 1 | 0 | 0 | 0 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  |  | 2 | 0 | 0 | 1 | 0 | 
To convert the hexadecimal number C29B... |  |  |  |  |  |  |  |  |  |  |  |  | 3 | 0 | 0 | 1 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  |  | 4 | 0 | 1 | 0 | 0 | 
 |  |  | C | 2 | 9 | B |  |  |  |  |  |  | 5 | 0 | 1 | 0 | 1 | 
 |  |  | 1100 | 0010 | 1001 | 1011 |  |  |  |  |  |  | 6 | 0 | 1 | 1 | 0 | 
 |  |  |  |  |  |  |  |  |  |  |  |  | 7 | 0 | 1 | 1 | 1 | 
C29B in Hexadecimal = 1100001010011011 in Binary |  |  |  |  |  |  |  |  |  |  |  |  | 8 | 1 | 0 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  |  |  |  | 9 | 1 | 0 | 0 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  |  | A (10) | 1 | 0 | 1 | 0 | 
 | Example B |  |  |  |  |  |  |  |  |  |  |  | B (11) | 1 | 0 | 1 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  |  | C (12) | 1 | 1 | 0 | 0 | 
 |  |  |  |  |  |  |  |  |  |  |  |  | D (13) | 1 | 1 | 0 | 1 | 
 |  |  |  |  |  |  |  |  |  |  |  |  | E (14) | 1 | 1 | 1 | 0 | 
 |  |  |  |  |  |  |  |  |  |  |  |  | F (15) | 1 | 1 | 1 | 1 | 

## Slide 18: Hexadecimal to Decimal Decimal to Hexadecimal
The easiest way to convert Hexadecimal to Decimal and Decimal to Hexadecimal is to convert to Binary as an intermediate step.
(Unless of course you use a calculator)